## Slide 1: User Program and System Call

## Slide 2: Outline
Kernel Threads and User Processes
MIPS Simulator
Nachos User Programs
Implementation of Nachos System Calls

## Slide 3: Kernel Threads and User Processes
What is Kernel?
  smallest core of operating system
  provides basic services to other parts of OS and user processes
    process management
    memory management
    file system and networking
  The code of kernel runs in the system mode.

## Slide 4: Kernel Threads and User Processes
Threads in the Nachos Kernel
  Each thread has its own stack for procedure calls of the kernel code.
  Each thread has its own register state to save kernel registers for the context switch between threads.
  All kernel threads share the code (program) of the kernel.

## Slide 5: Kernel Threads and User Processes
What is a User Process?
  A process running a user program (not part of kernel) in its address space.
  It has its own user stack for procedure calls of the user code.
  It has its own user register state to save user registers during the context switch between user processes.
  It normally runs its own code in the user mode.
  It invokes system calls to run kernel code in the system mode.
  When it runs the kernel code, it is a kernel thread.
  User process = Kernel thread + Address space + User register state

## Slide 6: Kernel Threads and User Processes
Nachos user process
  class Thread {
    private:
      int* stackTop; // the current stack pointer
      _int machineState[MachineStateSize]; // all registers except for stackTop
    public:
    ...
  #ifdef USER_PROGRAM
    int userRegisters[NumTotalRegs]; // user-level CPU register state
    public:
      void SaveUserState(); // save user-level register state
      void RestoreUserState(); // restore user-level register state
      AddrSpace *space; // User code this thread is running.
  #endif
  };

## Slide 7: Outline
Kernel Threads and User Processes
MIPS Simulator
Nachos User Programs
Implementation of Nachos System Calls

## Slide 8: MIPS Simulator
Why simulator?
  To understand how an operating system works with hardware support of a machine, we need to see how
    MMU (memory management unit)
    system call instruction
    exception handling
  works in the machine.
  Machine simulator is a convenient way to do that.

## Slide 9: Modules of MIPS Simulator (/machine)
1. Machine (machine.cc/h)
2. Mipssim (mipssim.cc/h)
3. Translate (translate.cc/h)
4. Timer (timer.cc/h)
5. Interrupt (interrupt.cc/h)
6. Disk (disk.cc/h)
7. Console (console.cc/h)
8. Network (network.cc/h)
9. Statics (stats.cc/h)
10. Sysdep (sysdep.cc/h)
11. Utility (thread/utility.cc/h)
模拟计算机需要：
CPU指令集及指令执行
虚拟地址转换
时钟
各种中断
磁盘
输入输出设备
网络
系统资源使用统计
兼容硬件抽象

## Slide 10: MIPS Simulator
MIPS Machine Simulator
  The components of the machine:
  class Machine {
    public:
    ...
    char *mainMemory; // physical memory to store user program,
    // code and data, while executing
    int registers[NumTotalRegs]; // CPU registers, for executing user programs
    TranslationEntry *tlb; // this pointer should be considered
    // "read-only" to Nachos kernel code
      TranslationEntry *pageTable;
      unsigned int pageTableSize;
    private:
    ...
  };

## Slide 11: MIPS Simulator
Memory access functions
  bool ReadMem(int addr, int size, int* value); // Read or write 1, 2, or 4 bytes of virtual
  bool WriteMem(int addr, int size, int value); // memory (at addr). Return FALSE if a
  // correct translation couldn't be found.
Register access functions
  int ReadRegister(int num); // read the contents of a CPU register
  void WriteRegister(int num, int value); // store a value into a CPU register
Address translation function
  ExceptionType Translate(int virtAddr, int* physAddr, int size, bool writing);
  // Translate an address, and check for
  // alignment. Set the use and dirty bits in
  // the translation entry appropriately,
  // and return an exception code if the
  // translation couldn't be completed.

## Slide 12: MIPS Simulator
Exception Handling function
  void RaiseException(ExceptionType which, int badVAddr);
  // Trap to the Nachos kernel, because of
  // a system call or other exception.
Machine run simulation
  // Routines callable by the Nachos kernel
  void Run(); // Run a user program
  void OneInstruction(Instruction *instr); // Run one instruction of a user program.

## Slide 13: MIPS Simulator
More Details of MIPS Simulations
  Machine instruction: represents both undecoded and decoded forms of an instruction
  class Instruction {
  public:
      void Decode(); // decode the binary
      // representation of the instruction
      unsigned int value; // binary representation of the instruction
      char opCode; // Type of instruction. This is NOT the
      // same as the opcode field from
      // the instruction: see defs in mips.h
      char rs, rt, rd; // Three registers from instruction.
      int extra; // Immediate or target or shamt field or offset.
      // Immediates are sign-extended.
  };

## Slide 14: MIPS Simulator
running the user program
  void Machine::Run() {
    Instruction *instr = new Instruction; // storage for decoded instruction
    if(DebugIsEnabled('m'))
    printf("Starting thread \"%s\" at time %d\n",
    currentThread->getName(), stats->totalTicks);
    interrupt->setStatus(UserMode);
    for (;;) {
    OneInstruction(instr);
    interrupt->OneTick();
    if (singleStep && (runUntilTime <= stats->totalTicks))
    Debugger();
    }
  }

## Slide 15: MIPS Simulator
Simulation of one machine instruction
  void Machine::OneInstruction(Instruction *instr) {
    int raw;
    int nextLoadReg = 0;
    int nextLoadValue = 0; // record delayed load operation, to apply in the future
    // Fetch instruction
    if (!machine->ReadMem(registers[PCReg], 4, &raw))
    return; // exception occurred
    instr->value = raw;
    instr->Decode();
    ...
    // Compute next pc, but don't install in case there's an error or branch.
    int pcAfter = registers[NextPCReg] + 4;
    int sum, diff, tmp, value;
    unsigned int rs, rt, imm;

## Slide 16: MIPS Simulator
// Execute the instruction (cf. Kane's book)
switch (instr->opCode) {
  case OP_ADD:
  sum = registers[instr->rs] + registers[instr->rt];
  if (!((registers[instr->rs] ^ registers[instr->rt]) & SIGN_BIT) &&
  ((registers[instr->rs] ^ sum) & SIGN_BIT)) {
  RaiseException(OverflowException, 0);
  return;
  }
  registers[instr->rd] = sum;
  break;
  ...
  case OP_SYSCALL:
  RaiseException(SyscallException, 0);
  return;
  ...
  default: ASSERT(FALSE);
} // Now we have successfully executed the instruction.
Notes: // If there is any kind of exception or interrupt, we invoke the
// exception handler, and when it returns, we return to Run(), which
// will re-invoke us in a loop. This allows us to
// re-start the instruction execution from the beginning, in
// case any of our state has changed. On a syscall,
// the OS software must increment the PC so execution begins
// at the instruction immediately after the syscall.
When the processor attempts to execute an instruction and it results in an exception, the kernel exception handler is invoked. The kernel must tell the processor where this exception handler is by invoking setExceptionHandler(). If the exception resulted from a syscall instruction, it is the kernel's responsibility to advance the PC register, which it should do by calling advancePC().

## Slide 17: MIPS Simulator
  // Do any delayed load operation
  DelayedLoad(nextLoadReg, nextLoadValue);
  // Advance program counters.
  registers[PrevPCReg] = registers[PCReg]; // for debugging, // in case we are jumping
  // into lala-land
  registers[PCReg] = registers[NextPCReg];
  registers[NextPCReg] = pcAfter;
  }

## Slide 18: MIPS Simulator
Simulation of Exception Handling
  change to the system mode
  call the corresponding exception handler according to the type of the exception.
  void Machine::RaiseException(ExceptionType which, int badVAddr) {
    DEBUG('m', "Exception: %s\n", exceptionNames[which]);
    // ASSERT(interrupt->getStatus() == UserMode);
    registers[BadVAddrReg] = badVAddr;
    DelayedLoad(0, 0); // finish anything in progress
    interrupt->setStatus(SystemMode);
    ExceptionHandler(which); // interrupts are enabled at this point
    interrupt->setStatus(UserMode);
  }

## Slide 19: Outline
Kernel Threads and User Processes
MIPS Simulator
Nachos User Programs
Implementation of Nachos System Calls

## Slide 20: Nachos User Programs
How to Make Binary Executables of Nachos User Programs
Compile MIPS assembly program start.s to MIPS object module
Compile C programs into MIPS object modules
Link the object modules to form the load module in COFF
Convert the load module to use NOFF format

## Slide 21: Nachos User Programs
Start program start.s
  It provides the top level code as the starting point to control the calls to main() function and Exit() system call after the main() function is finished.
  It provides the assembly code implementation of all the Nachos system calls (11 of them).

## Slide 22: Nachos User Programs
  #define IN_ASM
  #include "syscall.h"
    .text
    .align 2
    .globl _start
    .ent _start
  _start:
    jal main
    move $4,$0
    jal Exit /* if we return from main, exit(0) */
    .end _start
    .globl Halt
    .ent Halt
  Halt:
    addiu $2,$0,SC_Halt
    syscall
    j $31
    .end Halt
    .globl Exit
    .ent Exit
Notes: S4到$7 寄存器存放系统调用的参数
$2寄存器存放系统调用码
$31寄存器存放返回地址，jal 。。。会把返回地址放到$31中

## Slide 23: Nachos User Programs
  Exit:
    addiu $2,$0,SC_Exit
    syscall
    j $31
    .end Exit
    .globl Exec
    .ent Exec
  ...
    .globl _main
    .ent _main
  _main:
    j $31
    .end _main

## Slide 24: Nachos User Programs
Nachos System Call Interfaces in C
  There are 11 Nachos system calls whose prototypes are defined in ../userprog/syscall.h
  These C functions are implemented by assembly code because they need to use instruction syscall to trap into the kernel to complete the services required.
  Any Nachos user C program using these system calls need to include this file.

## Slide 25: Nachos User Programs
  #ifndef SYSCALLS_H
  #define SYSCALLS_H
  #include "copyright.h"
  /* system call codes -- used by the stubs to tell the kernel which system call
  * is being asked for */
  #define SC_Halt 0
  #define SC_Exit 1
  #define SC_Exec 2
  #define SC_Join 3
  #define SC_Create 4
  #define SC_Open 5
  #define SC_Read 6
  #define SC_Write 7
  #define SC_Close 8
  #define SC_Fork 9
  #define SC_Yield 10

## Slide 26: Nachos User Programs
  #ifndef IN_ASM
  void Halt();
  void Exit(int status);
  typedef int SpaceId;
  SpaceId Exec(char *name);
  int Join(SpaceId id);
  typedef int OpenFileId;
  #define ConsoleInput 0
  #define ConsoleOutput 1

## Slide 27: Nachos User Programs
  void Create(char *name);
  OpenFileId Open(char *name);
  void Write(char *buffer, int size, OpenFileId id);
  int Read(char *buffer, int size, OpenFileId id);
  void Close(OpenFileId id);
  void Fork(void (*func)());
  void Yield();
  #endif /* IN_ASM */
  #endif /* SYSCALL_H */

## Slide 28: Nachos User Programs
What does a compiled C program look like?
  Use MIPS gcc cross-compiler with -S to generate the assembly code of the C program.
  ../test/halt.c program
    #include "syscall.h"
    int main()
    {
      Halt();
      /* not reached */
    }
  type make halt.s in ../test/
    $ make halt.s
    >>> Compiling .s file for halt.c <<<
    /usr/local/mips/bin/decstation-ultrix-gcc -G 0 -c -I../userprog -I../threads -S -c -o halt.s halt.c

## Slide 29: Nachos User Programs
halt.s generated
    .file 1 "halt.c"
    gcc2_compiled.:
    _gnu_compiled_c:
      .text
      .align 2
      .globl main
      .ent main
    main:
      .frame $fp,24,$31 # vars= 0, regs= 2/0, args= 16, extra= 0
      .mask 0xc0000000,-4
      .fmask 0x00000000,0
      subu $sp,$sp,24
      sw $31,20($sp)
      sw $fp,16($sp)
      move $fp,$sp
      jal _main
      jal Halt
    $L1:
      move $sp,$fp
      lw $31,20($sp)
      lw $fp,16($sp)
      addu $sp,$sp,24
      j $31
      .end main
Notes: Args 16 +fp 4 +ra 4 =24

## Slide 30: Outline
Kernel Threads and User Processes
MIPS Simulator
Nachos User Programs
Implementation of Nachos System Calls

## Slide 31: Implementation of Nachos System Calls
Implementation of Nachos System Calls
  All system call functions issue the syscall instruction with system call code store in register $2.
  Exception handling hardware
    changes the user mode to the system mode
    invokes the appropriate exception handling routine in the kernel to do the job
    change the system mode back to the user mode
  Exception handling routine
    part of the kernel
    function ExceptionHandler(ExceptionType which)

## Slide 32: Implementation of Nachos System Calls
  void ExceptionHandler(ExceptionType which) {
  int type = machine->ReadRegister(2);
  if ((which == SyscallException) && (type == SC_Halt)) {
  DEBUG('a', "Shutdown, initiated by user program.\n");
  interrupt->Halt();
  } else {
  printf("Unexpected user mode exception %d %d\n", which, type);
  ASSERT(FALSE);
  }
  }

## Slide 33: Implementation of Nachos System Calls
Process management system calls
  typedef int SpaceId: unique identifier for each executing user program (address space).
  SpaceId Exec(char *name): Start a new user process (and its address space) to execute the binary executable named name in the Nachos root directory and return its SpaceId.
  void Exit(int status): Terminate this user program with exit status in status.
  int Join(SpaceId id): Return immediate if the user process with SpaceId id has already terminated; otherwise block this calling user process until it is terminated. Return value is the exit status of the user process with SpaceId id.

## Slide 34: Implementation of Nachos System Calls
User-level thread management system calls
  void Fork(void (*func)()): Create or fork a new thread to execute function func() within the address space of this user process.
  void Yield(): Yield the CPU to another runnable thread, whether in this address space or not.

## Slide 35: Implementation of Nachos System Calls
File-system system calls
  typedef int OpenFileId: definition of open file descriptor
  void Create(char *name): Create a new file named name.
  OpenFileId Open(char *name): Open the file named name and return its open file descriptor.
  void Write(char *buffer, int size, OpenFileId id): Write "size" bytes from "buffer" in the user program to the open file.
  int Read(char *buffer, int size, OpenFileId id): Read "size" bytes from the open file into "buffer" in the user program. Return the actual number of bytes read.
  void Close(OpenFileId id): Close the open file.

## Slide 36: Implementation of Nachos System Calls
Context Switch Between User Processes
  Suppose that a user process calls system call Yield() and kernel is to do context switch from this user process to another user process (or to another user thread of the same user process).
  What should be done to make this context switch?
    1. save the user registers of the current user process
    2. save the address space of the current user process
    3. save the kernel register of the current thread
    4. load the kernel register of the next thread
    5. load the user register of the next process
    6. restore the address space of the next process (page table)

## Slide 37: Implementation of Nachos System Calls
void Scheduler::Run (Thread *nextThread) {
Thread *oldThread = currentThread;
#ifdef USER_PROGRAM // ignore until running user programs
  if (currentThread->space != NULL) { // if this thread is a user program,
    currentThread->SaveUserState(); // save the user's CPU registers
    currentThread->space->SaveState();
  }
#endif

## Slide 38: Implementation of Nachos System Calls
  oldThread->CheckOverflow(); // check if the old thread
  // had an undetected stack overflow
  currentThread = nextThread; // switch to the next thread
  currentThread->setStatus(RUNNING); // nextThread is now running
  SWITCH(oldThread, nextThread);
  if (threadToBeDestroyed != NULL) {
    delete threadToBeDestroyed;
    threadToBeDestroyed = NULL;
  }
#ifdef USER_PROGRAM
  if (currentThread->space != NULL) { // if there is an address space
    currentThread->RestoreUserState(); // to restore, do it.
    currentThread->space->RestoreState();
  }
#endif
}

## Slide 39: Implementation of Nachos System Calls
How a User Process is started?
  Nachos command to run a user program: nachos -x name
  main(int argc, char **argv) {
  ...
  for (argc--, argv++; argc > 0; argc -= argCount, argv += argCount) {
  ...
  #ifdef USER_PROGRAM
  if (!strcmp(*argv, "-x")) { // run a user program
  ASSERT(argc > 1);
  StartProcess(*(argv + 1));
  argCount = 2;
  } else if (!strcmp(*argv, "-c")) { // test the console
  ...
  }
  #endif // USER_PROGRAM
  ...
  }
  currentThread->Finish(); // NOTE: if the procedure "main"
  return(0); // Not reached...
  }

## Slide 40: Implementation of Nachos System Calls
A function StartProcess() to start a user process
  create the address space for the user program
  make the current thread a user process
  initialize user registers and machine page table
  change to the user mode
  jump to run user code pointed by the user PC
    void StartProcess(char *filename) {
      OpenFile *executable = fileSystem->Open(filename);
      AddrSpace *space;
      if (executable == NULL) {
      printf("Unable to open file %s\n", filename);
      return;
      }
      space = new AddrSpace(executable);

## Slide 41: Implementation of Nachos System Calls
      currentThread->space = space;
      delete executable; // close file
      space->InitRegisters(); // set the initial register values
      space->RestoreState(); // load page table register
      machine->Run(); // jump to the user progam
      ASSERT(FALSE); // machine->Run never returns;
      // the address space exits
      // by doing the syscall "exit"
    }

## Slide 42: Implementation of Nachos System Calls
InitRegisters() function of AddrSpace
  clear all user registers
  set the user PCReg to 0 and NextPC to 4
  set user stack pointer StackReg to the bottom of the user stack.
  void AddrSpace::InitRegisters() {
    int i;
    for (i = 0; i < NumTotalRegs; i++)
    machine->WriteRegister(i, 0);
    machine->WriteRegister(PCReg, 0);
    machine->WriteRegister(NextPCReg, 4);
    machine->WriteRegister(StackReg, numPages * PageSize - 16);
  }
Notes: // Set the stack register to the end of the address space, where we
// allocated the stack; but subtract off a bit, to make sure we don't
// accidentally reference off the end!

## Slide 43: Implementation of Nachos System Calls
Set machine page table point to the page table of the user process
    void AddrSpace::RestoreState()
    {
    machine->pageTable = pageTable;
    machine->pageTableSize = numPages;
    }

## Slide 44: Thanks!